## Slide 1: Digital Logic Design
0
Lecture#1
Instructor: Nasir Ali
Slides Courtesy: Mr. Syed Usman Lecturer

## Slide 2: Grading Policy
1
Assignments/ Projects (16%)
4 Assignments.
Quizzes (14%)
4 (Announced/ Unannounced) quizzes
Mid Exam (30%)
Final (40%)

## Slide 3: Digital Systems
2
Digital systems represent information using a binary system, where data can assume one of only two possible values:
zero or one.
Appropriate for implementation in electronic circuitry, where values are characterized by the absence/presence of an electrical current flow.

## Slide 4: Analog signals
3
These are usually older electronic gadgets (introduced before the mid 1990’s).
A good example of an analog signal is the loud-speaker of a stereo system. When the volume is turned up the sound increases slowly and constantly.
Examples of analog systems include; Old radios, megaphones and the volume control on old telephone hand sets.

## Slide 5: Digital signals
4
Modern electronic products such as computers and mobile phones depend on digital signals.
The signal is sent as a series of ‘on’ and ‘off’ pulses.
The signal is either present or it is not.

## Slide 6: Advantages of Digital System
5

## Slide 7: Digital to Analog Systems
6

## Slide 8: Analog to Digital Systems
7

## Slide 9: Binary Digits and Logic Levels
8

## Slide 10: Digital Waveform
9

## Slide 11: Digital Waveform (cont.)
10

## Slide 12: Periodic Pulse Waveforms
11

## Slide 13: Timing Diagrams
12

## Slide 14: Logic Gates
13
Digital systems are said to be constructed by using logic gates.
These gates are the AND, OR, NOT, NAND, NOR, XOR and XNOR gates.
The basic operations are described below with the aid of Truth Tables.

## Slide 15: Logic Gates
14
The AND gate is an electronic circuit that gives a high output (1) only if all its inputs are high.
A dot (.) is used to show the AND operation i.e. A.B.
AND gate

## Slide 16: Cont.
15
OR gate
The OR gate is an electronic circuit that gives a high output
(1) if one or more of its inputs are high.
A plus (+) is used to show the OR operation.

## Slide 17: Cont.
16
NOT gate
The NOT gate is an electronic circuit that produces an inverted version of the input at its output.
It is also known as an inverter.

## Slide 18: Binary Arithmetic Operations
17
Binary Addition
It is a key for binary subtraction, multiplication, division.
Binary Subtraction
Subtraction and Borrow, these two words will be used very frequently for the binary subtraction.

## Slide 19: Binary Multiplication
18
Binary multiplication is similar to decimal multiplication.
It is simpler than decimal multiplication because only 0s and 1s are involved.

## Slide 20: Number System
19
Binary Number System
Octal Number System
Decimal Number System
Hexa-Decimal Number System

## Slide 21: 20 Binary Number System
Binary numbers uses only 0 and 1 digits.
Example:

## Slide 22: Octal Number System
21
Octal numbers uses digits from 0 to 7.
Example:

## Slide 23: Decimal Number System
22
Decimal numbers uses digits from 0 to 9.
Example:

## Slide 24: Hexadecimal Numbers
23
Hex numbers uses digits from 0 to 9 and A to F.
Example:

## Slide 25: Number System Conversion Table
24
DecimalBase- 10 | BinaryBase-2 | OctalBase-8 | HexadecimalBas e-16
0 | 0 | 0 | 0
1 | 1 | 1 | 1
2 | 10 | 2 | 2
3 | 11 | 3 | 3
4 | 100 | 4 | 4
5 | 101 | 5 | 5
6 | 110 | 6 | 6
7 | 111 | 7 | 7
8 | 1000 | 10 | 8
9 | 1001 | 11 | 9
10 | 1010 | 12 | A
11 | 1011 | 13 | B
12 | 1100 | 14 | C
13 | 1101 | 15 | D
14 | 1110 | 16 | E
15 | 1111 | 17 | F

## Slide 26: Decimal to Other Base System
25
Step 1 − Divide the decimal number to be converted by the value of
the new base.
Step 2 − Get the remainder from Step 1 as the rightmost digit (least significant digit) of new base number.
Step 3 − Divide the quotient of the previous divide by the new base.
Step 4 − Record the remainder from Step 3 as the next digit (to the left) of the new base number.
Repeat Steps 3 and 4, getting remainders from right to left, until the
quotient becomes zero in Step 3.
The last remainder thus obtained will be the Most Significant Digit
(MSD) of the new base number.

## Slide 27: Example
26
Step | Operation | Result | Remainder
Step 1 | 29 / 2 | 14 | 1
Step 2 | 14 / 2 | 7 | 0
Step 3 | 7 / 2 | 3 | 1
Step 4 | 3 / 2 | 1 | 1
Step 5 | 1 / 2 | 0 | 1
Decimal Number: (29)10
Calculating Binary Equivalent −

## Slide 28: Cont.
27
As mentioned in Steps 2 and 4, the remainders have to be arranged in the reverse order so that the first remainder becomes the Least Significant Digit (LSD) and the last remainder becomes the Most Significant Digit (MSD).
Decimal Number − (29)10 = Binary Number − (11101)2.

## Slide 29: Example 2
28

## Slide 30
Class Task
29
Decimal Number: (22)10

## Slide 31: Class Task Solution
30

## Slide 32: Binary to Decimal
31
Step | Binary Number | Decimal Number
Step 1 | 11101 | ((1 × 24) + (1 × 23) + (1 × 22) + (0 × 21) + (1 × 20))
Step 2 | 11101 | (16 + 8 + 4 + 0 + 1)
Step 3 | 11101 | 29
Binary Number − 111012 Calculating Decimal Equivalent −
Binary Number − (11101)2 = Decimal Number − (29)10

## Slide 33
Example 2
32
Binary Number − (1111101)2.

## Slide 34
Class Task
33
Binary Number − (110101)2.

## Slide 35: Class Task Solution
34

## Slide 36: Octal to Binary
35
Step | Octal Number | Decimal Number
Step 1 | 25 | ((2 × 81) + (5 × 80))
Step 2 | 25 | (16 + 5 )
Step 3 | 25 | 21
Octal Number − (25)8
Step 1 − Convert to Decimal
Octal Number − (25)8 = Decimal Number − (21)10

## Slide 37: Octal to Binary (Cont.)
36
Step | Operation | Result | Remainder
Step 1 | 21 / 2 | 10 | 1
Step 2 | 10 / 2 | 5 | 0
Step 3 | 5 / 2 | 2 | 1
Step 4 | 2 / 2 | 1 | 0
Step 5 | 1 / 2 | 0 | 1
Step 2 − Convert Decimal to Binary
Decimal Number (21)10 = Binary Number − (10101)2
Octal Number (25)8 = Binary Number (10101)2

## Slide 38: Direct Method: Binary to Octal
Step | Binary Number | Octal Number
Step 1 | 10101 | 010 101
Step 2 | 10101 | 2 5
Step 3 | 10101 | 25
37
Step 1 − Divide the binary digits into groups of three (starting from the right).
Step 2 − Convert each group of three binary digits to one octal digit.
Example
Binary Number − (10101)2 Calculating Octal Equivalent
Binary Number (10101)2 = Octal Number (25)8

## Slide 39: Direct Method: Octal to Binary
38
Step | Octal Number | Binary Number
Step 1 | 25 | 2 5
Step 2 | 25 | 010 101
Step 3 | 25 | 010101
Step 1 − Convert each octal digit to a 3 digit binary number.
Step 2 − Combine all the resulting binary groups (of 3 digits each) into a single binary number.
Example
Octal Number − (25)8
Calculating Binary Equivalent −
Binary Number (25)8 = Octal Number (010101)2

## Slide 40: Direct method: Binary to Hexadecimal
39
Step | Binary Number | Hexadecimal Number
Step 1 | 10101 | 0001 0101
Step 2 | 10101 | 1 5
Step 3 | 10101 | 15
Step 1 − Divide the binary digits into groups of four (starting from the right).
Step 2 − Convert each group of four binary digits to one hexadecimal symbol.
Example
Binary Number − (10101)2
Binary Number (10101)2 = Hexadecimal Number (15)16

## Slide 41: Direct Method: Hexadecimal to Binary
40
Step | Hexadecimal Number | Binary Number
Step 1 | 15 | 1 5
Step 2 | 15 | 0001 0101
Step 3 | 15 | 00010101
Step 1 − Convert each hexadecimal digit to a 4 digit binary number (the hexadecimal digits may be treated as decimal for this conversion).
Step 2 − Combine all the resulting binary groups (of 4 digits each) into a single binary number.
Example: Hexadecimal Number − (15)16
Calculating Binary Equivalent
Hexadecimal Number (15)16 = Binary Number (10101)2

## Slide 42: Hexadecimal to Octal
41
Hexadeci mal = | A | 2 | D | E | 
Binary = | 1010 | 0010 | 1101 | 1110 | = 10100010 11011110 binary
When converting from hexadecimal to octal, it is often easier to first convert the hexadecimal number into binary and then from binary into octal.
For example, to convert A2DE hex into octal:
Add leading zeros or remove leading zeros to group into sets of three binary digits.
Binary: 1010001011011110 = 001 010 001 011 011 110
Then, look up each group in a table:

## Slide 43: Cont.
42
Binary = | 001 | 010 | 001 | 011 | 011 | 110 | 
Octal = | 1 | 2 | 1 | 3 | 3 | 6 | = 121336 octal
Binary: | 000 | 001 | 010 | 011 | 100 | 101 | 110 | 111
Octal: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Through a two-step conversion process, hexadecimal A2DE
equals binary 1010001011011110 equals octal 121336.

## Slide 44: Octal to Hexadecimal
43
Octal = | 3 | 4 | 5 | 
Binary = | 011 | 100 | 101 | = 011100101 binary
When converting from octal to hexadecimal, it is often easier to first convert the octal number into binary and then from binary into hexadecimal.
For example, to convert 345 octal into hex:
Drop any leading zeros or pad with leading zeros to get groups of four binary digits (bits):
Binary 011100101 = 1110 0101
Then, look up the groups in a table to convert to hexadecimal
digits.

## Slide 45: Cont.
44
Binary: | 0000 | 0001 | 0010 | 0011 | 0100 | 0101 | 0110 | 0111
Hexad ecimal: | 0 | 1 | 2 | 3 | 4 | 5 | 6 | 7
Binary: | 1000 | 1001 | 1010 | 1011 | 1100 | 1101 | 1110 | 1111
Hexad ecimal : | 8 | 9 | A | B | C | D | E | F
Therefore, through a two-step conversion process, octal 345 equals binary 011100101 equals hexadecimal E5.

## Slide 46: One’s Complement
45
Take one’s complement of 1010110
1111111
-1010110
Answer ???

## Slide 47: Two’s complement
46
Take two’s complement of 1010110
Answer??